## Slide 1: WHEN GOOD BUILDINGS GO BAD
Chris Chapman, CIH
“ There are no sick buildings – only mismanaged ones”
Dr. Mike Berry – USEPA (ret.)

## Slide 2: Common Environmental Issues for Schools (review)
Asbestos – general comment - compliance issues with EPA AHERA 40 CFR 763 (along with Virginia DOE, BCOM, VOSH)
Radon in Schools (Code of Virginia (CV) Section § 22.1-138) mandatory testing of all school buildings for radon in accordance with EPA.
Lead in drinking for all school buildings (CV Sections § 22.1-135.1. Potable water; lead testing)
Lead in Paint EPA AHERA (40 CFR 745) RRP Rules for Renovation buildings built prior to 1978; Children 6 and under
Notes: Asbestos – ahera reports typically used for reno/demo – even 3 yr reinspections – out of date; self serving but if relying on a management plan which has never been updated – should think about just redoing. House-keeping are doing annual notice; 6 month surveillance; all kinds of hidden acms;
Radon – should be redone if alter building configuration such as addition/renovation/mech upgrade; do testing during colder months – october – march; follow ansi/aarst with adequate number of samples – each office/classroom; increase samples if space greater 2 k sq ft; need proper amount of dups/blanks/spikes
Lead in drinking water – 3 ts - testing all taps used for consumption – can exclude lab sinks, bathrooms etc; recommend redo every 4-5 yrs; priority older schools; new fixtures can have lead – china
Lead based paint – us epa rrp rule – covers child occupied facilities – 6 and under – tricky to comply – renovations in elementary schools would be covered; a number of other compliance pieces go along with this; but basic issue – do a good survey – hud surface by surface using an xrf; OSHA ?
MMS NOTES
RADON: Per VDOE, EPA recommends testing in “all frequently-occupied rooms that are in contact with the ground” (e.g., classrooms, offices, gymnasiums, auditoriums, and cafeterias but not storage rooms, stairwells, toilets, closets, kitchens, hallways)
(B), pertaining to radon, has been in this Code section since 1993-94
Supt Memo (2014): VDH recommends the following practices:
If building or addition opened after July 1, 1994, must test for radon; new buildings or additions should be tested within 18 months of occupancy
Test pursuant to EPA-402-R-92-014 “Radon Measurement in Schools”
  Either internal staff trained to comply OR a contractor certified by the National Radon Safety Board of National Radon Proficiency Program testers
Conduct testing in all classrooms contacting the ground
Test on days school is in session and HVAC system(s) operating normally
Test between Nov 1 and March 31
If result is ≥ 4.0pCi/L: retest. If elevated levels confirmed on retest, mitigation should occur
LEAD
Supt memo: use laboratory certified by Department of General Services’ Division of Consolidated Laboratory Services

## Slide 3: New Virginia Regulation IAQ
(Code of Virginia (CV) Chapter 9 Section § 22.1-141.3 - 22.1-141.9)
Designated responsible individual oversee public school buildings with respect to implementation; and indoor air quality - Dir of Facilities?
EPA – most common factors in good IAQ
source control, lack of mechanically supplied ventilation, proper filtration
ANSI/ASHRAE general recc for fresh outside air for schools 10 cfm/person (lower for some common areas)
Notes: MMS NOTES:
AIR QUALITY/VENTILATION:
VDOE guidelines state the “school’s heating, ventilation, and air conditioning (HVAC) system is the most important internal system in a school facility” – a major energy user in a school and “may also impact learning or comfort of the building occupants”
VDOE guidelines also require HVAC systems in school to meet current ASHRAE standards (American Society of Heating, Refrigeration, and Air-Conditioning Engineers
Chris discuss impacts of CO2, relative humidity, CO, temp on humans (physical impacts; facility impacts like development of mold) and ASHRAE standards generally?
Carbon monoxide detectors: required by enactment of the 2021 General Assembly. At least one. Best placed at places where there is combustion (boiler room, cafeteria)
NEW Statutory scheme (2025):

## Slide 4: AIR QUALITY
VDOE Guidelines for School Facilities for Ventilation: must meet ASHRAE standards
ANSI/ASHRAE 62.1 – adequate fresh outside air
ANSI/ASHRAE 55 – acceptable temperature and RH conditions
Va. Code § 22.1-138.2: Each school building that was built before 2015 and that houses any classrooms for students should be equipped with at least one carbon monoxide detector
Notes: MMS: VDOE guidelines state the “school’s heating, ventilation, and air conditioning (HVAC) system is the most important internal system in a school facility” – a major energy user in a school and “may also impact learning or comfort of the building occupants”
VDOE guidelines also require HVAC systems in school to meet current ASHRAE standards (American Society of Heating, Refridgeration, and Air-Conditioning Engineers
Chris discuss impacts of CO2, relative humidity, CO, temp on humans (physical impacts; facility impacts like development of mold) and ASHRAE standards generally.
Carbon monoxide detectors: required by enactment of the 2021 General Assembly. At least one. Best placed at places where there is combustion (boiler room, cafeteria)

## Slide 5: INDOOR AIR QUALITY Virginia Code § 22.1-141.3 et seq.
141.3: scope and purpose
141.4: definitions
141.5: inspection and evaluation program of the indoor air quality in each school at least once every 4 school years; records publicly available
Set up for a mechanical contractor or Mech PE (not CIH) for checking
For Facility Managers – EPA IAQ Tools for Schools a good General resource
Available on line for free – this a more global look at IAQ but an overview of best practices to maintain good indoor the school
Notes: MMS: 2025: new Article (4) added to the Chapter on School Property: Indoor Air Quality: inspection and Evaluation
141.3: scope of article = provisions of this article apply to matters relating to indoor air quality in public school buildings occupied by school board employees and students during regular work and school hours
141.4: definitions
141.5 2 year inspection, records publicly available

## Slide 6: INDOOR AIR QUALITY Virginia Code § 22.1-141.5
(A) “review, inspection, or evaluation” of
HVAC systems per ANSI/ASHRAE 62.1
Other hazards to look at (as good practice or by other statue); These include but are not limited to
Potential for exposure to microbiological airborne particles (incl. fungi, mold, bacteria)
Air contaminants (incl. vapors from paint, cleaning chemicals, particulates, outdoor air pollutants)
Degree of pest infestation (incl. insects and rodents)
Degree of pesticide usage
Presence/plans for removal of “extremely hazardous substances” per 42 U.S.C. 11002(a)(2)
Moisture incursion
Overall cleanliness of facilities
Structural elements (incl. roofing, basements, slabs)
Use of space, particularly areas designed to be unoccupied
(B) Results publicly available at regularly scheduled SB meeting and on individual school’s website
Notes: MMS: What constitutes the (internal) “inspection and evaluation program of the indoor air quality” – list
ALSO, affirmatively “publicly available” – not just FOIA-ble ... Must be shared at a SB meeting and posted on the individual school’s website

## Slide 7: INDOOR AIR QUALITY Virginia Code § 22.1-141.6
“industry-recognized uniform inspection and evaluation” of HVAC, every 4 years
  “certified testing, adjusting, and balancing technician;”
  Certified industrial hygienist;
  Technician with master HVAC license from DPOR; or
  Mechanical engineer
  List of items to be tested/evaluated: filter efficiency, outside air delivery rate, condition/operation of ventilation system, outside/return/supply air measurements, maintenance of ventilation, CO2...
Goal: identify extent to which ventilation systems provide appropriate ventilation (ASHRAE standards)
publicly available: SB meeting and website
Notes: MMS: AND, every four years, ” – more formal/external(?) “industry-recognized uniform inspection and evaluation” of HVAC system in each school building
ALSO, affirmatively “publicly available” – not just FOIA-ble ... Must be shared at a SB meeting and posted on the individual school’s website

## Slide 8: Common IAQ Concerns in School Buildings
# 1 Mold - Allergies are most common effect
Mild transitory responses to severe chronic illness
Effects dependent on a variety of factors, including
  Age
  Health
  Individual sensitivity
  Genetic predisposition
#2 Poor Ventilation – lack of fresh outside air;
CO2 > 1000 ppm – general guideline
Elevated CO2 – GENALLY Not an immediate health hazard; these conditions may be indicative of the buildup of a variety of indoor contaminants that can cause discomfort in some individuals.

## Slide 9: Not so common
Mystery odors / sensitive individuals
VOC, Particulate
CO
Bacteria
Sewage odors ‘ dry traps
Dirty sock syndrome/HVAC system

## Slide 10: Aging Buildings and Environmental Concerns Legal Requirements and Enforcement
October 2025
Mandi Montgomery Smith
The Education Law Group
.
© 2025

## Slide 11: OSHA Regulations
“General Industry” 29 C.F.R. 1910
Walking/working surfaces
Exit routes/emergency planning
Powered platforms/manlifts
Environmental
Ventilation
Noise
Hazardous materials
PPE
General (sanitation, marking hazards, confined spaces)
Medical and first aid
Fire Protection
Compressed gas/equipment
Materials handling and storage
“Construction” 29 C.F.R. 1926
Machinery and Machine Guarding
Hand and Portable Power Tools
Welding, Cutting, Brazing
Toxic and Hazardous Substances
Notes: So far, we have covered environmental safety prescriptions in law that are primarily focused on students. Not all of those have an independent basis for “enforcement” – no direct private right of action other than a negligence action. (for which there would the possibility of sovereign immunity)
Criminal? § 22.1-292. Penalties on officers and teachers. Any division superintendent, member of a school board or other school officer or any principal or teacher in a public school violating any provision of this title shall be guilty of a Class 4 misdemeanor if no other penalty is prescribed.
How they get more often seem to get enforced is through OSHA (VOSH), which has a panoply of regulations protective of employees.
OSHA regulations are categorized partly by industry – special rules for maritime, agriculture, … schools fall into “general industry” and possibly “construction” if the violation is related to a construction project at a facility the division owns. Within each industry, there are subcategories of topical regulations.
Within “General industry,” for example, I’ve listed the subcategories – many details within the requirements: MSDS labels, procedures for “confined space entry,” requirements for PPE, toxic/hazardous substances (including asbestos, carbon mono and dioxides, lead …)

## Slide 12: Administrative Enforcement

## Slide 13: Complaint-driven Investigation
1 | Complaint to VOSH
2 | Inspections
3 | Interviews
4 | Requests for documentation
5 | Closing conference; Inspector submits proposed citations to Regional Director
Notes: Once VOSH has a complaint over which they have jurisdiction, they investigate.
Inspections: CAN BE (usually are?) unannounced
Code allows for warrant (with probable cause, issued from judge)
Inspections are NOT limited to the subject matter of the complaint – if your complaint is about walking/working surfaces, they will ask about your MSDS safety sheets, training on other topics, etc.
Interviews: you will not necessarily be aware of who the investigator speaks with during OR after
Inspector has “closing conference,” is supposed to discuss all items in citation during conference
Inspector then sends citation to regional director

## Slide 14: Employee Protections against Retaliation Virginia Code § 40.1-51.2:1
Making any complaint to employer or third party regarding safety and health provisions of Title 40.1
Instituting or causing to be instituted proceedings relating to safety and health provisions of Title 40.1
Testifying or intending to testify in any such proceeding
Cooperating with or providing information during worksite inspection
Exercising on his own behalf of on behalf of any other employee any right afforded by the safety and health provisions of Title 40.1

## Slide 15: Notice of Citation
Lists proposed violations and penalties
Must be posted for employees at/near location of alleged violation
  For 3 days or until abated (whichever is longer)
  Penalty amounts can be redacted … but FOIA
Offers resolution paths
  Contest (within 15 work days)
  Informal Conference
  Abate and pay (Agree)
Must be issued within 6 months of alleged violation
Virginia Code § 40.1-49.4(A)(!)
Notes: Analogy: Stopped for speeding ticket. The yellow carbon copy (I’m old!) is your notice of citation. It tells you (a) you can prepay … maybe or (b) the court date which allows you to go talk to the judge
The notice is NOT an official finding and penalty unless you fail to contest
POSTING requirement: at site of alleged violation or where affected employees will see – for 3 days or until abated, whichever is longer
Penalty amounts can be redacted BUT someone can make a FOIA request to DOLI and will get unredacted
-- If officially “Union,” employee rep gets a copy in addition to posting; technically, if employees have specifically designated a rep
VOSH has a 6 month SOL – cannot cite after 6 months 40.1-49.4(A)(3)
RESOLUTION PATHS
Contest (within 15 days)
Informal conference
Abate and pay (within deadlines set in notice)

## Slide 16: Contest
No later than 15 workdays from delivery of citation
In whole or in part
Penalties, abatement periods, violations
Posted with citation
Notes: Penalties due within 15 days UNLESS you contest; if contest, not due until final decision (settlement agreement and corresponding final order from DOLI Commissioner … or circuit court ruling)
STRONGLY ENCOURAGED to contest within 5 work days of receipt of citation -- if not contested, becomes FINAL order and can no longer be challenged/amended by agency or court 40.1-49.4(C)
Typically will result in agreed/negotiated resolution that becomes final order.
CONTESTED citations that are not settled by agreement go to court.
EMPLOYEES can also contest abatement date

## Slide 17: Informal Conference
Notify employees of time and place
Right to attend
Present documentation
Abatement steps
Amendments
Contest facts/argument
Notes: Is really a settlement conference/mediation of sorts. In my experience, conversational/informal.
Opportunity to:
Obtain clearer understanding of the specific standards that apply
Obtain a better explanation of violations cited
Discuss ways to correct violations
Discuss questions re proposed penalty
Discuss how penalty is calculated and any mitigating circumstances which might affect the proposed penalty
Discuss problems with abatement dates
Discuss problems concerning employee safety and health practices
Obtain answers to any other related questions
Employee representative has the opportunity to participate in informal conference – must post notice of time/place at same place citation was posted.

## Slide 18: Categories of Citation
Serious
Other-than-serious
Repeat
Willful
Notes: SERIOUS = accident or illness could occur which would most likely result in death or serious physical harm, unless employer did not know or could not have known of violation. MAX PENALTY = $15,875/viol
OTHER-THAN-SERIOUS = direct relationship to job safety and health, but not a serious violation. MAX PENALTY = $15,875/viol
REPEAT = repeated after prior final order against same employer for same or substantially similar violation of the standard/rule/regulation within past 3 years. MAX PENALTY = $158,725/viol
WILLFUL = (A) intentional and knowing (as opposed to inadvertent) violation and employer was “conscious” that what he was doing constituted a violation OR (B) employer – though not consciously committing violation – was aware that hazardous condition existed and made no reasonable effort to eliminate the condition. MAX PENALTY = $158,725/viol
CRIMINALLY WILLFUL is willful that resulted in death. MAX PENALTY = $70,000 and/or IMPRISONMENT up to 6 mos. DOLI can recommend Commonwealth’s attorney pursue manslaughter charges
DE MINIMUS = no direct or immediate relationship to safety and health  no actual citation, no penalty.

## Slide 19: Penalty Adjustment Factors
Size of Employer
Gravity of Violation
Good Faith
History
Notes: Penalty adjustment factors
SIZE OF EMPLOYER = “small business” (unlikely to apply to public schools), based on total employees at all sites
1-25 eees: 70% reduction
26-100 eees: 40%
101-250: 20%
>251: 0 reduction
GRAVITY: the more hazardous/more likely to result in employee injury or illness  higher penalty
GOOD FAITH: up to 25% reduction to recognize employer’s good faith
HISTORY: no citation for serious, willful or repeated in prior 3 years  10% reduction

## Slide 20: Agree
Abate within abatement period
Pay (15 work days)
Report on Corrective Action
Notes: Interest accrues on “past-due” (from date penalty becomes “final”), but are waived if paid within 30 calendar days of final order date

## Slide 21: Failure to Settle
VOSH refers to Commonwealth’s Attorney
Complaint in Circuit Court
Default judgment or bench trial
Appeal to Court of Appeals
Notes: if CONTESTED citations are not settled by agreement, VOSH refers the matter to the Commonwealth’s Attorney and files a civil action in circuit court. Commonwealths Attorney required to represent Commonwealth in VOSH case
Bench trial – affirms, modifies, vacates citation and proposed penalty
“affected employees” or their representatives may participate as “parties”
VOSH can also file for injunction (mandatory/affirmative or prohibitive) of conditions/practices at the workplace. Even an ex parte order but only for 5 days

## Slide 22: Failure to Contest
Final Order
No further challenge/amendment
Payment of penalties in proposed Citation due
Notes: if not contested, becomes FINAL order and can no longer be challenged/amended by agency or court 40.1-49.4(C)
Proposed penalties become final and due in 15 work days.

## Slide 23: Private Rights of Action

## Slide 24: Private/Personal Injury Claims
Personal Injury
By accident
Arising out of and in the course of employment
Duty
Breach
Causation
Damage/injury
Personal Injury
Workers Comp
Notes: PRIVATE claims – generally would be personal injury tort (if student); WC if employee
Complications on the PI/tort side: Duty (probably) – breach (possibly...) – damage/injury (?) – causation (???) ... AND, sovereign immunity (absolute for SB; from all but gross negligence claims for employees/agents)
Complications on the WC side: injury (probably) – “accident” (???) – arising out of/in course of employment (???)
ALSO, statutes of limitations generally are 2 years from injury for both types of claim, but can vary under circumstances – minors have extended period; some types of occupational diseases compensable under WC may have a delay as well.
Also, Injunction attempted ...

## Slide 25: Non-Retaliation/Whistleblower Protections
Discharge or other discriminatory/adverse action
Because employee engaged in protected action (filed a complaint, testified, exercised other rights)
Notes: Whistleblower protections exist in VOSH, WC, and IN GENERAL (Fraud and Abuse Whistleblower Protection Act, Bowman doctrine)
The claims would, generally, take this form as a civil lawsuit. For a VOSH retaliation: complaint with commissioner (VOSH) and VOSH pursues in court.
WC process- claimant sues directly on own behalf
Whistleblower sues directly on own behalf.
Remedies for successful claimant:
Reinstatement/restraining order
Back pay and interest (8%)
Attys fees and costs
Whistleblower act also has “civil penalties” between 500 and 2500 paid to a Reward Fund for whistleblowers

## Slide 26: Questions?

## Slide 27: Sample of School-Specific Statutes/Regulations

## Slide 28: RADON
Virginia Code § 22.1-138(B)
By July 1, 1994, every
school building in operation
in the Commonwealth shall be tested for radon pursuant to procedures established by the U.S. Environmental Protection Agency (EPA) for radon measurements in schools.
School buildings and additions opened for operation after July 1, 1994, shall be tested for radon pursuant to such EPA procedures and regulations prescribed by the Board of Education pursuant to subsection A. Each school shall maintain files of its radon test results and make such files available for review. The division superintendent shall report radon test results to the Department of Health.
Notes: Per VDOE, EPA recommends testing in “all frequently-occupied rooms that are in contact with the ground” (e.g., classrooms, offices, gymnasiums, auditoriums, and cafeterias but not storage rooms, stairwells, toilets, closets, kitchens, hallways)
(B), pertaining to radon, has been in this Code section since 1993-94
Supt Memo (2014): VDH recommends the following practices:
If building or addition opened after July 1, 1994, must test for radon; new buildings or additions should be tested within 18 months of occupancy
Test pursuant to EPA-402-R-92-014 “Radon Measurement in Schools”
  Either internal staff trained to comply OR a contractor certified by the National Radon Safety Board of National Radon Proficiency Program testers
Conduct testing in all classrooms contacting the ground
Test on days school is in session and HVAC system(s) operating normally
Test between Nov 1 and March 31
If result is ≥ 4.0pCi/L: retest. If elevated levels confirmed on retest, mitigation should occur

## Slide 29: MOLD
Virginia Code § 22.1-138(D)
Each local school board
shall develop and implement
a plan to test and, if necessary, a plan to remediate mold in public school buildings in accordance with guidance issued by the U.S. Environmental Protection Agency. Each local school board shall (i) submit such testing plan and report the results of any test performed in accordance with such plan to the Department of Health and (ii) take all steps necessary to notify school staff and the parents of all enrolled students if testing results indicate the presence of mold in a public school building at or above the minimum level that raises a concern for the health of building occupants, as determined by the Department of Health.
Notes: Amendment to -138 passed during 2020 session, to become effective July 1, 2021 (both mold and Legionnaires)
VDH resources re prevention – moisture control, and how to select a contractor/mold specialist

## Slide 30: WATER QUALITY
Virginia Code § 22.1-138(C)
Develop and maintain a water management program for prevention of Legionnaires’ disease at each public school building in division;
Validate the water management plan at least annually;
Maintain files related to the water management program, including results of all validation and remediation activities, if any, and make such files open for review.
Notes: Per VDOE guidance, Legionella bacteria are commonly spread through airborne water droplets (mist or vapor), which can come from whirlpool spas, team locker shower areas, cooling towers, and water used for drinking and bathing. Causes a form of pneumonia if inhaled or aspirated. The bacteria has been found in schools’ mechanical equipment, specifically outside cooling towers. No federal requirement to test or protocols for frequency of testing, or action thresholds if bacteria is found.
The water management program identifies hazardous conditions and takes steps to minimize growth/spread of Legionella and other waterborne pathogens in building water systems: maintain water temps outside the ideal range for Legionella; prevent stagnation; ensure adequate disinfection; maintain systems to prevent scale, corrosion, and biofilm growth (which provide a habitat and nutrients for Legionella)
Amendment to -138 passed during 2020 session, to become effective July 1, 2021

## Slide 31: LEAD Virginia Code § 22.1-135.1
Each local school board shall develop and implement a plan to test and, if necessary, remediate potable water from sources identified by the U.S. Environmental Protection Agency as high priority for testing, including bubbler-style and cooler-style drinking fountains, cafeteria or kitchen taps, classroom combination sinks and drinking fountains, and sinks known to be or visibly used for consumption. Such plan shall be consistent with guidance published by the U.S. Environmental Protection Agency or the Department of Health. The local school board shall give priority in the testing plan to schools whose school building was constructed, in whole or in part, before 1986. Each local school board shall submit such testing plan and report the results of any such test to the Department of Health. Each local school board shall take all steps necessary to notify parents if testing results indicate lead contamination that exceeds 10 parts per billion.
Notes: First enacted in 2017; last 2 sentences and reference to EPA guidance added in 2020
Supt memo: use laboratory certified by Department of General Services’ Division of Consolidated Laboratory Services

## Slide 32: ASBESTOS
Asbestos Hazard Emergency Response Act
42 C.F.R. Part 763
Inspect facilities for ACM (initial and then once/3 years)
Prepare management (AHERA) plan (maintain and update)
Annual notification to parent, teacher, employee organizations re availability of the plan and any asbestos-related actions taken or planned in the facility
Designate a compliance person
Take action to prevent or reduce asbestos hazards
Personnel working with asbestos must be trained and accredited (inspectors, compliance, custodians)
If removal of asbestos will occur during renovation or demolition, comply with National Emissions Standards for Hazardous Air Pollutants (NESHAP) re asbestos

## Slide 33: Plans for Crisis/Emergencies
Virginia Code § 22.1-279.8
Required, “to prevent, manage, and respond to a critical event or emergency, including … spills or other exposures to hazardous substances…”
Requires designation of an “Emergency Manager” for every division